TIME LENGTH : around 1 min

ADLC

1) Each Filter
2) No. Of False Positives
3) Changing of Parameters to Reduce no. Of False positives

Initially, The number of false positives were found to be too high. For example out of a 704 image set, the number of false positives were found to be 94.The false positives were primarily comprised of stones, bushes , uneven land masses and sometimes cars.

By changing the parameters of MSER function (such as maximum and minimum area of potential targets ,maximum variation and delta), The number of false positives were reduced.

Then the color filter (which makes use of the k-means clustering algorithm) was then tuned to reject images which consist of more than two dominant colors since the targets to be detected contains 2 colors only.

There were issues in detecting the color purple. It was often detected as blue instead. To rectify this, the camera settings (such as ISO, Shutter speed and Aperture) were tuned to get a more clear picture with well defined color.

For shape detection , the hue moments of some shapes such as rectangle and trapezoid had the same values. Hence changes were made based on emperical test results to get the number of vertices for successful shape detection.

Time taken--- 1:05

The images are first scanned for targets and then extracted using the Maximally stable extremal Region (MSER) algorithm. /

This is followed by color classification which makes use of the k-means clustering algoritm. Post the clustering algorithm, if the image ( i.e extracted target ) has more than two dominant colors , it is rejected as a false positive.

 This is followed by shape classification where the targets are examined for convexity and their hu invariant moments are computed. Using these values, the targets are classified into their respective shapes.

If a valid shape, then the image is passed on for optical character recogonition and localization.